## Slide 1
Multi-Modal SLAM Proxy: Fusing 2D LiDAR and Depth Camera for Robust Mapping
Sensor Fusion for Autonomous Robot Navigation
ROS 2 Humble · RTAB-Map · LiDAR + RGB-D + IMU
Karthik Prabu Natarajan (1564587) · Snehamol Sunny (1568233)
Invigilator: Prof. Dr. Peter Nauth

## Slide 2
OVERVIEW
Project Overview
🎯 Objective
Build and evaluate a multi-modal sensor fusion SLAM architecture in a simulated warehouse environment using ROS 2 and Gazebo.
⚙️ Platform
BCR Bot — open-source differential drive robot using 2D LiDAR, RGB-D camera, and IMU sensors.
🔗 Approach
Fuse complementary sensing technologies via EKF + RTAB-Map to improve robustness of simultaneous localization and mapping.
🧪 Evaluation
Compare multi-modal vs single-sensor configurations across map quality, trajectory stability, loop closure, and CPU efficiency.

## Slide 3
SYSTEM DESIGN
System Architecture
2D LiDAR
/scan
RGB-D Camera
/depth/image_raw
/rgb/image_raw
IMU
/imu
Wheel Odom
/odom
EKF Odometry Fusion
RTAB-Map (Graph-Based SLAM)
Visual odometry · Loop closure · Pose graph optimization
Occupancy Map
/map
Pose Estimate
/localization_pose
Loop Closures
/rtabmap/loop_closure

## Slide 4
METHODOLOGY
Sensor Suite & EKF Fusion
📡
2D LiDAR
/scan
✦ 10 Hz planar scans
Primary role
Loop Closure
Key strength
Works in darkness
Output
Geometric constraints
Captures surrounding geometry via laser ranging. Forms the backbone for scan matching and structural consistency checks.
📷
RGB-D Camera
/depth + /rgb
✦ Dense depth + color
Primary role
Visual Odometry
Key strength
Feature-rich motion
Output
Frame-to-frame pose
Generates synchronized color and depth images for visual odometry and environmental representation.
🔩
IMU + Wheel Odom
/imu + /odom
✦ High-freq stabilization
Primary role
EKF Motion Prior
Key strength
Short-term stability
Output
/odometry/filtered
Fused via Extended Kalman Filter to produce a smoothed motion prior, reducing drift during rotational maneuvers.
IMU + Wheel Odometry → EKF (robot_localisation) → /odometry/filtered → RTAB-Map motion prior

## Slide 5
METHODOLOGY
RTAB-Map Localization Framework
Why RTAB-Map?
Natively supports heterogeneous sensor fusion combining LiDAR and RGB-D within a single unified graph-SLAM framework. Chosen for its ability to evaluate the multi-modal fusion goal of this project.
Dual-Path Data Flow
VISUAL PATH (RGB-D Camera)
→ Extract visual features (edges, textures)
→ Frame-to-frame pose estimation
→ Dense local map representation
GEOMETRIC PATH (2D LiDAR)
→ ICP scan matching for global consistency
→ Loop closure detection & triggers
→ Pose graph update on revisit
Both paths converge in Graph-SLAM optimization

## Slide 6
IMPLEMENTATION
Implementation Details
A Simulation Setup
· ROS 2 Humble + Gazebo simulation engine
· Warehouse world loaded via URDF robot descriptions
· Gaussian noise injected into all simulated sensors
B Nav2 Stack Integration
C Transform Tree (TF2)
map
└─ odom
└─ base_link
└─ laser_frame / camera_link
· RTAB-Map projects dense 3D cloud to 2D /map occupancy grid
· Nav2 global + local cost maps consume the occupancy grid
· Local map uses rolling window with synchronized sensor streams
· MapsToPose action goals confirmed SLAM output usability

## Slide 7
EXPERIMENTS
Experimental Setup
Sensor Fusion
LiDAR + RGB-D + IMU
LiDAR Only
2D LiDAR
Camera Only
RGB-D Camera
Simulation
ROS 2 Humble + Gazebo small warehouse world. Repeatable controlled runs without physical hardware constraints.
Bot Sensors
2D LiDAR (σ = 0.01 m Gaussian noise), RGB-D camera depth + color, and IMU at high frequency.
Physics Modelling
Wheel friction (μ₁, μ₂), inertia tensors, and URDF-defined constraints to closely mimic real-world slippage.
Blackout Simulation
Gazebo directional sun model disabled mid-run. reduces RGB-D feature extraction to zero organically without killing the ROS node.
All sensors use Gaussian noise models to prevent over-fitting to perfect simulation data.

## Slide 8
RESULTS
Sensor Configuration Comparison
Camera Only
▸ Near-total mapping failure in darkness
▸ Visual odometry lost without light
▸ No loop closure without features
▸ High CPU efficiency but unusable
LiDAR Only
▸ Full boundary traced; no tracking loss
▸ Loop closure achieved repeatedly
▸ Dense false-positive closure mesh
▸ ICP graph saturation → unstable
Multi-Modal Sensor Fusion
▸ Clean occupancy map + stable path
▸ Visual + geometric complementarity
▸ Survived sensor blackout seamlessly
▸ ICP switched in when RGB-D failed

## Slide 9
KEY FINDING
Dynamic Sensor Blackout Test
Midway through navigation, the Gazebo environment lighting was completely disabled sinking the warehouse into darkness and reducing RGB-D visual feature extraction to zero.
The RTAB-Map hybrid strategy seamlessly shifted localization weight to ICP scan-matching from the active 2D LiDAR.
The system supported spatial localization without any coordinate jumps, odometry drift, or map fragmentation.
Blackout Timeline
t = 0
Navigation Start
Full multi-modal fusion active — LiDAR + RGB-D + IMU
Lights Out
Gazebo lighting disabled. RGB-D feature extraction drops to zero.
t = end
Stable Finish
ICP takes over seamlessly. Map integrity preserved.

## Slide 10
Camera-Only Performance
Lidar-Only Performance
Sensor- Fusion Performance
RESULTS
SLAM Graph Comparison

## Slide 11
RESULTS
Quantitative Metric Results
TABLE I — Absolute Trajectory Error (ATE)
Sensor Configuration
Mean ATE (m)
RMSE ATE (m)
Max ATE (m)
Std Dev (m)
Multi-Modal Fusion (LiDAR + RGB-D + IMU)
0.031
0.034
0.082
0.012
LiDAR-Only
0.097
0.103
0.251
0.031
Camera-Only
0.289
0.341
1.820
0.178
TABLE II — Relative Pose Error (RPE, Δ = 1 s)
Sensor Configuration
Mean RPE (m/s)
RMSE RPE (m/s)
Max RPE (m/s)
Std Dev (m/s)
Multi-Modal Fusion (LiDAR + RGB-D + IMU)
0.018
0.027
0.041
0.009
LiDAR-Only
0.044
0.051
0.138
0.024
Camera-Only
0.173
0.219
0.812
0.142

## Slide 12
TABLE III — Time-Segmented Blackout Breakdown (Multi-Modal Fusion)
Phase
Active Modality
Mean ATE (m)
Mean RPE (m/s)
Pre-Blackout (0–45 s)
LiDAR + RGB-D
0.024
0.014
Blackout Transition
ICP fallback
0.038
0.047
During Blackout (45–110 s)
LiDAR (ICP)
0.039
0.022
Overall Degradation
—
Δ +0.015 m
Δ +0.008 m/s
  RESULTS

## Slide 13
CHALLENGES
Key Challenges Encountered
1
Timestamp Synchronization
2
LiDAR-Only Loop Closure Saturation
3
RTAB-Map Database Corruption
4
Computational Load (ICP Density)

## Slide 14
CONCLUSION
Key Takeaways
01
Fusion Wins
Multi-modal (LiDAR + RGB-D + IMU) achieved the highest overall viability score of 22, outperforming all single-sensor baselines.
02
Complementary Strengths
LiDAR provides stable geometric constraints under poor lighting; RGB-D delivers dense motion estimation covering each other's weaknesses.
03
Graceful Degradation
The Proxy Architecture survived a complete visual blackout by autonomously shifting to ICP, no map fragmentation or trajectory jumps.
04
LiDAR-Only Limitations
Geometry only SLAM over-saturates the Graph-SLAM optimizer with false-positive loop closures in repetitive warehouse environments.

## Slide 15
  SOURCE CODE
GitHub link Hosting the Project source code, Report, presentations and demo video is
https://github.com/karthikprabu810/sensor-fusion
Thank you!